## Slide 1
Draft Environmental Impact Statement Summary Presentation by the Louis Berger Group for Sterling Forest Resort
Public Hearing Pursuant to State Environmental Quality Review Act
Tuxedo, New York
December 4, 2014
Notes: Good evening. My name is Larry Pesesky. I am a senior vice president with Louis Berger, one of the consulting firms retained by RW Orange County to prepare the draft environmental impact statement for its proposed Sterling Forest Resort. I will present a high-level, approximately 15-minute summary of of the DEIS content on behalf of RW Orange County.

## Slide 2: Outline
Project Description
Project Purpose & Need
Project Alternatives
Environmental Impact & Mitigation Measures
Notes: My presentation will cover these items. You are encouraged to view the document on the Town’s website – www.tuxedogov.org.

## Slide 3: Project Site
Notes: The project site consists of private property, known as “Ren-Faire Properties,” located in the northwest corner of the Town of Tuxedo, straddling NY State Route 17A. The parcels comprising the site total about 240 acres.

## Slide 4: Project Description
Mix of resort uses (highlights)
  1,000-room Resorts World Grand Hotel, six-to-seven stories tall, with casino (on abandoned landing strip)
  World Fairgrounds (on existing New York Renaissance Faire site)
  Ski Village (on existing Tuxedo Ridge Ski Center)
  Re-established Sterling Gardens
Ancillary Uses
  Dining and lodging-related commercial uses
  Arboretum
  2,500-seat amphitheater
  Funicular inclined railway
  Zip lines
  Toboggan run
  Snowboard pipes and rails
  Indian Kill Riverfront Walk
Notes:   An “Integrated Resort” is proposed with these uses with multiple attractions for gaming and non-gaming guests across all age groups
  The resort setting would make this a global destination for an estimated 7.8 million new visitors, that would be different from existing casinos in Northeast.

## Slide 5: Proposed Access and Parking
Proposed new Interchange 15B on I-87/New York Thruway at Route 106
  Subject to separate EIS under State Environmental Quality Review process
  Chapter X of the Resort DEIS contains a cumulative impact assessment covering the combined impact of the Resort and Interchange
Total of 8,786 parking spaces (net increase of 5,786 spaces over existing)
Two grade-separated pedestrian bridges over Route 17A to connect the site’s activities

## Slide 6: Proposed Interchange 15B

## Slide 7: Project Purpose & Need
Meet the purpose and needs of the Upstate New York Gaming and Economic Development Act of 2013
  Create jobs: the Project would create over 4,000 full and part-time jobs
  Reduce unemployment in disadvantaged areas of the State: Hudson Valley has over 50,000 unemployed residents
  Enhance the State’s tourism industry
  Generate substantial revenue for public education and taxpayer relief
Be consistent with RW Orange County’s June 30 Application to the State in response to the Request for Applications (RFA) to Develop and Operate a Gaming Facility in New York State

## Slide 8: Project Alternatives
No-Build Alternative
  No changes from existing NY Renaissance Faire and Tuxedo Ridge Ski Center uses
  Does not meet the Purpose and Need
As-of-Right Alternative
  Redevelopment to the maximum allowed under existing zoning: 49 single-family residences on 177.2 acres
  Does not meet the Purpose and Need
Alternative Architectural Building Design
  Height of spires on hotel reduced from over 200 feet to 172 feet, consistent with the Scoping Document
  Otherwise, identical to the Proposed Project with increased mitigation

## Slide 9: Land Use, Zoning & Public Policy
No-Build Alternative
  Maintains existing land uses; consistent with zoning
  Does not advance economic development goals of the Town Comp Plan
  No anticipated impact on community character
As-of-Right Alternative
  Replaces existing land uses with residential; consistent with zoning
  Does not advance economic development goals of the Town Comp Plan
  No anticipated impact on community character
Proposed Project/Architectural Design Alternative
  Adds fuller use of the site; maintains existing land uses
  Consistent with Gaming Overlay Zoning District & Town Comprehensive Plan
  Potential impacts on community character mitigated through traffic mitigation and measures to minimize visibility

## Slide 10: Geology, Soils & Topography
No-Build Alternative
  No increase in development “footprint” or impact from site development
  Would not resolve soil erosion from existing site uses
As-of-Right Alternative
  Site development footprint of ~34 acres
  Less excavation than Proposed Project
Proposed Project/Architectural Design Alternative
  Additional development footprint of ~19 acres over ~27 acres of existing development, with limited excavation
  Mitigation through adherence to soil erosion and sediment control plan

## Slide 11: Groundwater Resources
No-Build Alternative
  Lack of stormwater management continues to reduce infiltration from pre-development levels
As-of-Right Alternative
  Depending on the residential design, potential impact could be similar to Proposed Project
Proposed Project/Architectural Design Alternative
  Potential construction period impact from subsurface construction and dewatering; potential permanent impact from increase in impervious surfaces and reduction in infiltration to groundwater
  Mitigated through such mitigation measures minimizing construction limits and avoiding introduction of contaminants to groundwater during construction, and infiltration from water recycled for irrigation

## Slide 12: Wetlands & Surface Waters
No-Build Alternative
  Lack of stormwater management continues to have soil erosion and sedimentation impact on wetlands and open waters
As-of-Right Alternative
  Potential fill/disturbance of 0.12 acre of an isolated wetland
Proposed Project/Architectural Design Alternative
  Potential fill/disturbance of 3.6 acres of wetlands
  Design changed to reduce level of wetland impact
  Mitigation, including restoration of 6.1 acres of previously disturbed wetlands, would produce a net increase in the acreage of on-site wetlands

## Slide 13: Vegetation & Wildlife
No-Build Alternative
  No change from existing impact, including no vegetative management to control invasive species
As-of-Right Alternative
  Potential impact on 25.15 acres of natural and vegetative communities; 7.03 acres of tree removal
Proposed Project/Architectural Design Alternative
  Potential impact on natural and vegetative communities
  Mitigation through preservation of undisturbed areas and vegetation management

## Slide 14: Stormwater Management
No-Build Alternative
  Existing 26.81 acres of impervious surfaces would remain without stormwater runoff management and treatment
As-of-Right Alternative
  15.11 acres of impervious surfaces with standard storwater management and treatment
Proposed Project/Architectural Design Alternative
  Increase of 31.96 acres of impervious surface cover over existing
  Potential impacts minimized through stormwater retention/filtration, green roofs, and 13.7 acres of permeable pavement for surface parking

## Slide 15: Water Supply
No-Build Alternative
  No change from existing demand
As-of-Right Alternative
  Demand expected to be well within United Water service capacity and substantially less than Proposed Project
Proposed Project/Architectural Design Alternative
  Water demand of less than half of the Indian Kill reservoir safe yield of 600,000
  Net effect on Indian Kill Reservoir inflows of ˂1% because of water recycling for irrigation and reintroduction to Reservoir catchment

## Slide 16: Wastewater
No-Build Alternative
  No change from existing impact from outmoded treatment facility
As-of-Right Alternative
  Assumed negligible impact and use of existing wastewater treatment plant
Proposed Project/Architectural Design Alternative
  Negligible impact as wastewater reclamation facility would treat sanitary flows to better than Class A water standards

## Slide 17: Energy Use & Infrastructure Capacity
No-Build Alternative
  No change; site remains served by electricity only
As-of-Right Alternative
  Negligible impact from electric consumption estimated between 7,236 and 9,600 kWh per month; assumed site remains served by electricity only
Proposed Project/Architectural Design Alternative
  Negligible impact relative to existing electricity and natural gas supplies
  Incorporates renewable energy through solar to meet at least 10% of development needs

## Slide 18: Visual Character & Aesthetic Resources
No-Build Alternative
  Expected continued local adverse impact due to degraded Ren Faire structures
As-of-Right Alternative
  Expected improved visual and aesthetic character over No-Build Alternative; less visual impact than other Build alternatives due to lower building heights
Architectural Design Alternative
  Design reduces potential impact by using colors and materials compatible with the surrounding landscape and environment
  Potentially significant visual impacts from Katrina Court and Hogback Mountain Trail
Proposed Project
  Design reduces potential impact by using colors and materials compatible with the surrounding landscape and environment
  Potential visual impacts from Katrina Court, Clinton Woods, Allis Trail, and Hogback Mountain Trail

## Slide 19: Traffic, Transportation & Parking
No-Build Alternative
  Ren Faire traffic impacts would continue including uncontroled pedestrian crossings of Route 17A, parking on the shoulder of Route 17A, and some intersections with unacceptable levels-of-service
  Continued traffic congestion on Route 17 through Town
As-of-Right Alternative
  Minimal traffic impacts; some intersections with unacceptable levels-of-service
  Continued traffic congestion on Route 17 through Town
Proposed Project/Architectural Design Alternative
  Substantial increase in volume and continuousness of trips generated by site
  Measures to minimize traffic impact include: construct Interchange 15B; construct roundabout at Routes 17/17A intersection; roundabout, Route 17A widening, and second entrance intersection at the site; adequate on-site parking; and two pedestrian bridges to connect the site portions
  Traffic relief on Route 17 through Town

## Slide 20: Noise
No-Build Alternative
  No change from existing
As-of-Right Alternative
  Minimal (˂3dB) impact from trips generated by residences, primarily during commuter peak periods
  No major stationary noise sources
Proposed Project/Architectural Design Alternative
  36 total residences in Clinton Woods and laurel Ridge would be impacted by increased nighttime traffic on Route 17A; noise mitigated through building/window insulation and other treatments
  Residences and parkland in the Project vicinity would experience noise impacts, primarily in late night hours, with a perceived relative change of up to a doubling of noise levels but at relatively low absolute levels consistent with a rural area; mitigation includes restriction on end time of amphitheater events, placement of snow guns away from residences at night, and shielding of HVAC equipment
  Existing sounds levels from I-87 in the East Village will increase, although imperceptibly, due to opening of Interchange 15B; previous studies conducted by the NYS Thruway Authority have identified an existing impact (without 15B), and the impact and mitigation will appropriately be assessed during the Interchange 15B EIS, with the traffic input to the analysis to include anticipated Resort traffic

## Slide 21: Air Quality
No-Build Alternative
  No change from existing impact
As-of-Right Alternative
  No exceedance of air quality standards from traffic-related or residential heating systems emissions
Proposed Project/Architectural Design Alternative
  Increased emissions from site uses but within air quality standards
  No potential for adverse impacts from off-site intersections and roadway segments affected by Project-generated traffic
  Mitigation of on-site sources include high-efficiency low-NOx boilers and CNG-fueled shuttle buses

## Slide 22: Community Services & Fiscal Impacts
No-Build Alternative
  No change from existing demand for services, expenditures, or revenues
As-of-Right Alternative
  Minimal adverse impact from increased demand for police, fire, emergency, and road maintenance services and corresponding expenditures
Proposed Project/Architectural Design Alternative
  Potential impact from increase in demand for police, Town court, fire (negative net fiscal impact for Tuxedo Joint Fire District), emergency, and road maintenance services and corresponding revenues; mitigation measures to be finalized during FEIS preparation
  Positive net fiscal impact for the Town of Tuxedo and Orange County

## Slide 23: Cultural Resources
No-Build Alternative
  No change in existing minimal, indirect impacts on archaeological sites
As-of-Right Alternative
  Potential for direct adverse impact to one archaeological site
Proposed Project/Architectural Design Alternative
  Potential impact to any archaeological sites with mitigation (data recovery) to be coordinated with government and Tribal authorities

## Slide 24: Solid Waste & Hazardous Materials
No-Build Alternative
  No change in solid waste generation from the site
As-of-Right Alternative
  Relatively low solid waste generation from residences
Proposed Project/Architectural Design Alternative
  Potential impact from construction solid waste per month and approximately four tons of solid waste generated by daily operations
  Impacts to be mitigated through program of sustainable purchasing and recycling to reduce waste

## Slide 25: Socioeconomics
No-Build Alternative
  No change in employment and regional economic effect of existing site uses regional
As-of-Right Alternative
  Potential for adverse effect on the local economy from the displacement of the Renaissance Faire to a location likely outside of Tuxedo
Proposed Project/Architectural Design Alternative
  Project would have a substantial regional employment effect due to the creation of over 4,000 permanent jobs
  Project would have a substantial beneficial effect on the local and regional economy from increased disposable income from above-market wages and benefits offered to employees and operational expenditures
  Most jobs would be filled by existing residents of the region creating negligible demand for new housing
  Existing business operations on the site would be enhanced and revitalized with a greater offering of entertainment options

## Slide 26
THANK YOU!